## Slide 1
C-CAT PREPARATION COURSE
Day 2: Boolean Algebra, Logic Gates & Storage Systems
Building Digital Foundations for C-DAC Entrance
Topics
Boolean Algebra | Logic Gates | Storage
Level
Foundation + C-CAT Exam Focus
Slides
21

## Slide 2
Boolean Algebra — Three Fundamental Operations
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
2
AND (A · B)
Output is 1 ONLY when BOTH inputs are 1
A · B = 1 iff A=1 AND B=1
Multiplication analogy: 1·1=1, 1·0=0
OR (A + B)
Output is 1 when ANY input is 1
A + B = 1 iff A=1 OR B=1
Addition (capped at 1): 1+1=1, 1+0=1
NOT (A')
FLIPS / inverts the input value
0'=1 1'=0
Complement / Bar: A̅ or ~A or A'
⚠ Boolean values: only 0 or 1 | AND = multiplication | OR = addition (max 1) | NOT = flip

## Slide 3
Boolean Algebra Laws — Complete Reference
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
3
Law Name
AND Form
OR Form
Identity
A · 1 = A
A + 0 = A
Null / Domination
A · 0 = 0
A + 1 = 1
Idempotent
A · A = A
A + A = A
Complement
A · A' = 0
A + A' = 1
Commutative
A · B = B · A
A + B = B + A
Associative
(A·B)·C = A·(B·C)
(A+B)+C = A+(B+C)
Distributive
A·(B+C) = A·B+A·C
A+(B·C) = (A+B)·(A+C)
Absorption
A·(A+B) = A
A+(A·B) = A
Double Negation
(A')' = A
(A')' = A
C-CAT Tip: Distributive & Absorption laws are most commonly tested in simplification problems!

## Slide 4
De Morgan's Theorems
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
4
Theorem 1
(A · B)' = A' + B'
"NOT of AND = OR of NOTs"
Theorem 2
(A + B)' = A' · B'
"NOT of OR = AND of NOTs"
Memory Trick:
"Break the bar, change the sign"
Step 1: Split the NOT bar over each variable | Step 2: Change AND ↔ OR

## Slide 5
Boolean Simplification — Step by Step
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
5
Start:
A · B + A · B'
←
Given expression
Step 1:
A · (B + B')
←
Distributive Law
Step 2:
A · 1
←
Complement Law (B + B' = 1)
Step 3:
A
←
Identity Law (A · 1 = A)
Result: A·B + A·B' simplifies to A

## Slide 6
AND Gate
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
6
A ──┐
D──► Y
B ──┘
Symbol: AND Gate
Truth Table
A
B
Y
0
0
0
0
1
0
1
0
0
1
1
1
Y = A · B
Output is 1 ONLY when ALL inputs are 1

## Slide 7
OR Gate
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
7
A ──╲
)──► Y
B ──╱
Symbol: OR Gate
Truth Table
A
B
Y
0
0
0
0
1
1
1
0
1
1
1
1
Y = A + B
Output is 1 when ANY input is 1

## Slide 8
NOT Gate
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
8
A ──▷○──► Y
Symbol: NOT Gate
Truth Table
A
Y
0
1
1
0
Y = A'
Flips / inverts the input

## Slide 9
NAND Gate
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
9
A ──┐
D○─► Y
B ──┘
Symbol: NAND Gate
Truth Table
A
B
Y
0
0
1
0
1
1
1
0
1
1
1
0
Y = (A · B)'
UNIVERSAL GATE Opposite of AND
UNIVERSAL GATE

## Slide 10
NOR Gate
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
10
A ──╲
)○─► Y
B ──╱
Symbol: NOR Gate
Truth Table
A
B
Y
0
0
1
0
1
0
1
0
0
1
1
0
Y = (A + B)'
UNIVERSAL GATE Opposite of OR
UNIVERSAL GATE

## Slide 11
XOR Gate
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
11
A ──╲
=)──► Y
B ──╱
Symbol: XOR Gate
Truth Table
A
B
Y
0
0
0
0
1
1
1
0
1
1
1
0
Y = A ⊕ B
Output is 1 when inputs are DIFFERENT

## Slide 12
XNOR Gate
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
12
A ──╲
=)○─► Y
B ──╱
Symbol: XNOR Gate
Truth Table
A
B
Y
0
0
1
0
1
0
1
0
0
1
1
1
Y = (A ⊕ B)'
Output is 1 when inputs are SAME

## Slide 13
All 7 Logic Gates — Master Reference Card
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
13
Gate
Symbol
Expression
Key Behavior
AND
D
Y=A·B
1 only when ALL=1
OR
)≥
Y=A+B
1 when ANY=1
NOT
▷○
Y=A'
Flips input
NAND
D○
Y=(A·B)'
Opposite of AND
NOR
)○
Y=(A+B)'
Opposite of OR
XOR
=)
Y=A⊕B
1 when DIFFERENT
XNOR
=)○
Y=(A⊕B)'
1 when SAME
NAND & NOR = Universal Gates (can build ANY other gate using only these)

## Slide 14
Universal Gates — Building Everything from NAND
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
14
NOT from 1 NAND
Connect both inputs together:
A ──┐
D○──► A'
A ──┘
Both inputs = A → Output = (A·A)' = A'
AND from 2 NANDs
NAND → NOT:
A ──┐
D○──┐
B ──┘ D○──► Y = A·B
──┘
First NAND gives (AB)', second inverts back
OR from 3 NANDs
NOT each input, then NAND:
A─D○─A' ──┐
D○──► Y = A+B
B─D○─B' ──┘
NOT A, NOT B, then NAND them
Similarly, NOR is also a Universal Gate — any circuit can be built using only NOR gates!

## Slide 15
Half Adder — Adding Two Single Bits
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
15
Half Adder Circuit
Two Inputs: A, B
Two Outputs: Sum, Carry
Sum = A ⊕ B (XOR Gate)
Carry = A · B (AND Gate)
Half Adder Truth Table
A
B
Sum
Carry
0
0
0
0
0
1
1
0
1
0
1
0
1
1
0
1
Limitation:
Cannot handle carry input from previous stage. For chained addition, we need a Full Adder.
1 XOR gate + 1 AND gate = Half Adder | Adds two single-bit numbers

## Slide 16
Full Adder — Adding with Carry Input
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
16
Full Adder
Three Inputs: A, B, Cin (Carry In)
Two Outputs: Sum, Cout (Carry Out)
Sum = A ⊕ B ⊕ Cin
Cout = AB + BCin + ACin
Built from 2 Half Adders + 1 OR gate
Full Adder Truth Table
A
B
Cin
Sum
Cout
0
0
0
0
0
0
0
1
1
0
0
1
0
1
0
0
1
1
0
1
1
0
0
1
0
1
0
1
0
1
1
1
0
0
1
1
1
1
1
1
Full Adder = handles carry propagation | Chain N Full Adders = N-bit Ripple Carry Adder

## Slide 17
SRAM vs DRAM — Comparison
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
17
Feature
SRAM
DRAM
Technology
Flip-Flops (6 transistors)
Capacitor + 1 Transistor
Speed
Very Fast
Slower
Cost
Expensive
Cheap
Density
Low (larger cells)
High (smaller cells)
Refresh
No refresh needed
Needs periodic refresh
Power
More (static current)
Less (leakage only)
Use Case
CPU Cache (L1, L2, L3)
Main Memory (RAM)
Volatility
Volatile
Volatile
C-CAT Tip: SRAM = Static = Cache = Fast = Expensive | DRAM = Dynamic = Main RAM = Refresh needed

## Slide 18
ROM Types — Evolution of Read-Only Memory
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
18
ROM
Read Only Memory
Factory programmed Cannot change
▶
PROM
Programmable ROM
One-time programmable Burn fuses
▶
EPROM
Erasable PROM
UV light erasable Quartz window
▶
EEPROM
Electrically Erasable PROM
Electrically erasable Byte-by-byte
▶
Flash
Flash Memory
Block erasable Type of EEPROM
◀─── Less Flexible More Flexible ───▶
C-CAT Exam Focus:
EPROM = UV erasable | EEPROM = Electrically erasable | Flash = Block erasable (type of EEPROM)

## Slide 19
Secondary Storage Devices — Comparison
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
19
Device
Type
Access
Speed
Capacity
HDD
Magnetic
Random
Moderate
1-20 TB
SSD
Flash
Random
Very Fast
256GB-8TB
CD
Optical
Sequential
Slow
700 MB
DVD
Optical
Sequential
Slow
4.7 GB
Blu-ray
Optical
Sequential
Moderate
25-50 GB
Tape
Magnetic
Sequential Only
Slow
Backup/TB+
SSD = No moving parts = faster, more durable | HDD = moving platters = cheaper per TB

## Slide 20
Storage Units — Data Measurement Hierarchy
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
20
1 Bit 0 or 1
Smallest unit of data
1 Nibble = 4 Bits
One hex digit
1 Byte = 8 Bits
One character (ASCII)
1 KB = 1024 Bytes
A short text file
1 MB = 1024 KB
A photo / short song
1 GB = 1024 MB
A movie / large app
1 TB = 1024 GB
Large hard drive
1 PB = 1024 TB
Data center scale
C-CAT TRAP WARNING!
1 KB = 1024 bytes, NOT 1000! | Always use powers of 2: 2¹⁰ = 1024

## Slide 21
Day 2 — Quick Revision & Key Takeaways
C-CAT Preparation | Day 2: Boolean Algebra, Logic Gates & Storage
21
De Morgan's Theorems
(AB)' = A'+B' | (A+B)' = A'·B' | Break bar, change sign
Universal Gates
NAND & NOR can build ANY other gate — most tested concept!
XOR Rule
Different inputs → 1 | Same inputs → 0 (XNOR)
Memory Types
SRAM = Cache (fast, expensive) | DRAM = Main RAM (needs refresh)
ROM Evolution
ROM → PROM → EPROM (UV) → EEPROM (Electrical) → Flash (Block)
Flash Memory
Type of EEPROM | Block erasable | Used in SSDs, USB drives, SD cards
Storage Units
1 KB = 1024 bytes (NOT 1000!) | Bit → Nibble → Byte → KB → MB → GB → TB → PB
Master these 21 slides and you own Day 2 of C-CAT prep!