## Slide 1
Day 1: Computer Evolution,
Architecture & Number Systems
C-CAT Preparation Course — Module 1
CDAC PG-DAC Entrance Preparation

## Slide 2
IPO Cycle — Input, Processing, Output
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
INPUT DEVICES Keyboard, Mouse, Scanner, Mic
CPU (PROCESSING)
ALU
Control Unit
Registers
MEMORY (RAM / Cache)
OUTPUT DEVICES Monitor, Printer, Speaker
STORAGE (HDD, SSD, USB)

## Slide 3
Computer Generations — Timeline Overview
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
1st Gen 1940-1956
Vacuum Tubes
2nd Gen 1956-1963
Transistors
3rd Gen 1964-1971
Integrated Circuits
4th Gen 1971-Present
Micro- processors
5th Gen Present+
AI / ULSI
1940
1956
1964
1971
Present
C-CAT Tip: Generations are classified by the primary electronic component used — know which technology belongs to which generation!

## Slide 4
First Generation (1940-1956): Vacuum Tubes
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
• Used Vacuum Tubes as the primary electronic component
• ENIAC — First general-purpose computer (30 tons, 18,000 vacuum tubes!)
• Programmed in Machine Language (binary 0s and 1s only)
• Enormous size — occupied entire rooms, consumed huge power
• Magnetic drum memory used for storage
• Examples: ENIAC, UNIVAC I, IBM 701, EDVAC
C-CAT Tip: ENIAC facts are frequently tested: 30 tons, 18,000 vacuum tubes, 1946. Also remember UNIVAC I was the first commercial computer.

## Slide 5
Second Generation (1956-1963): Transistors
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
• Transistors replaced vacuum tubes — smaller, faster, more reliable
• Cheaper and consumed much less power than 1st generation
• Assembly language introduced; also FORTRAN & COBOL (HLLs)
• Magnetic Core Memory used as primary memory
• Punched cards still used for input
• Examples: IBM 1401, IBM 7094, CDC 1604, UNIVAC 1108
C-CAT Tip: Transistor = 2nd Gen. FORTRAN (1957) and COBOL (1959) were born in this era. Magnetic core memory is the key storage tech here.

## Slide 6
Third Generation (1964-1971): Integrated Circuits
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
• Integrated Circuits (ICs) — many transistors on a single silicon chip
• Keyboard and Monitor introduced (replacing punched cards)
• High-Level Languages: BASIC, Pascal, C
• Time-sharing Operating Systems enabled multiple users
• Smaller, cheaper, more efficient than 2nd generation
• Examples: IBM 360 series, PDP-8, Honeywell 6000
C-CAT Tip: IC = 3rd Gen (not 4th!). IBM 360 is the most important example. Time-sharing OS started here.

## Slide 7
Fourth Generation (1971-Present): Microprocessors
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
• VLSI (Very Large Scale Integration) — entire CPU on a single chip
• Intel 4004 — first commercial microprocessor (1971)
• Personal Computers (PCs) became affordable for individuals
• GUI-based Operating Systems (Windows, Mac OS)
• Intel Evolution: 4004 → 8086 → 80386 → Pentium → Core i-series
• Examples: IBM PC, Apple Macintosh, modern desktops & laptops
C-CAT Tip: Intel 4004 (1971) = first microprocessor. VLSI is 4th Gen, ULSI is 5th Gen. Don't confuse IC (3rd) with VLSI (4th)!

## Slide 8
Fifth Generation (Present & Beyond): AI
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
• ULSI (Ultra Large Scale Integration) technology
• Parallel Processing & Superconductors
• Natural Language Processing (NLP) and understanding
• Machine Learning and Deep Learning capabilities
• Expert Systems and Knowledge-based computing
• Examples: IBM Watson, Google AlphaGo, ChatGPT, Self-driving cars
C-CAT Tip: 5th Gen = AI + ULSI. Focus areas: NLP, ML, parallel processing. This generation is about computers that THINK and LEARN.

## Slide 9
Computer Generations — Summary Table
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
Generation | Years | Technology | Language | Example
1st Generation | 1940-1956 | Vacuum Tubes | Machine Language | ENIAC, UNIVAC I
2nd Generation | 1956-1963 | Transistors | Assembly, FORTRAN | IBM 1401, IBM 7094
3rd Generation | 1964-1971 | ICs | BASIC, Pascal, C | IBM 360, PDP-8
4th Generation | 1971-Present | Microprocessors (VLSI) | C, C++, Java | IBM PC, Mac
5th Generation | Present+ | AI / ULSI | Python, NLP, ML | Watson, ChatGPT

## Slide 10
Classification by Size
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
MICRO- COMPUTER
──────────────────
PC, Laptop, Tablet Single user
MINI- COMPUTER
──────────────────
PDP-11, AS/400 Up to 200 users
MAINFRAME COMPUTER
──────────────────
IBM zSeries Thousands of users
SUPER- COMPUTER
──────────────────
PARAM, Fugaku Scientific computing
Increasing Size, Power & Cost →

## Slide 11
Classification by Data Handling
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
ANALOG
Processes continuous data (physical quantities) Measures: temperature, pressure, voltage Example: Speedometer, Oscilloscope
DIGITAL
Processes discrete binary data (0s and 1s) All modern PCs and servers are digital Example: Desktops, Laptops, Smartphones
HYBRID
Combination of Analog + Digital Analog input → Digital processing Example: ICU monitors, Petrol pump meters
C-CAT Tip: Digital = discrete (0/1), Analog = continuous. Hybrid combines both. ICU monitor is a classic hybrid example!

## Slide 12
Von Neumann Architecture — Block Diagram
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
INPUT UNIT
CPU (Central Processing Unit)
ALU (Arithmetic & Logic Unit)
CONTROL UNIT (Directs & Coordinates)
REGISTERS (PC, IR, ACC, MAR, MDR)
Internal Bus
OUTPUT UNIT
MEMORY UNIT (RAM / ROM)
System Bus (Address + Data + Control)

## Slide 13
CPU Internal Structure — Zoomed In
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
CENTRAL PROCESSING UNIT (CPU)
ALU — Arithmetic & Logic Unit
• Arithmetic: +, –, ×, ÷
• Logic: AND, OR, NOT, XOR
• Comparison: <, >, =, ≠
Control Unit — Directs & Coordinates
• Fetches instructions from memory
• Decodes instructions
• Controls data flow between units
REGISTERS — High-Speed Temporary Storage Inside CPU
PC Program Counter
IR Instruction Register
ACC Accumulator
MAR Memory Address Register
MDR Memory Data Register
FLAGS Status Register

## Slide 14
System Bus — Address, Data & Control
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
CPU (Processor)
MEMORY (RAM / ROM)
I/O Devices
ADDRESS BUS — Unidirectional (CPU → Memory)
DATA BUS — Bidirectional (CPU ↔ Memory)
CONTROL BUS — Bidirectional (CPU ↔ Memory)
C-CAT Tip: Address Bus is ONE-WAY (CPU→Memory). Data Bus and Control Bus are TWO-WAY. This is a very common C-CAT question!

## Slide 15
Memory Hierarchy — Speed vs. Cost vs. Size
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
Registers
Fastest | Smallest | Most Expensive
Cache (SRAM)
Very Fast | Small | Expensive
RAM (DRAM)
Fast | Medium | Moderate Cost
Secondary Storage (HDD / SSD)
Slowest | Largest | Cheapest
S P E E D
S I Z E
C-CAT Tip: Memory hierarchy order: Registers > Cache > RAM > Secondary Storage. Speed decreases, size increases going down.

## Slide 16
Volatile vs. Non-Volatile Memory
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
VOLATILE MEMORY
• RAM (Random Access Memory)
• Cache Memory (SRAM)
• CPU Registers
Data is LOST when power is OFF
VS
NON-VOLATILE MEMORY
• ROM (Read-Only Memory)
• HDD / SSD
• Flash Drives / USB
Data is RETAINED when power is OFF
C-CAT Tip: RAM = Volatile (lost on power off). ROM, HDD, SSD = Non-Volatile (data retained). Cache is also volatile!

## Slide 17
Four Number Systems — Overview
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
Number System | Base (Radix) | Digits Used | Example | Use Case
Binary | 2 | 0, 1 | 1010₂ | Machine-level, digital circuits
Octal | 8 | 0-7 | 752₈ | Compact binary (3-bit groups)
Decimal | 10 | 0-9 | 459₁₀ | Human counting (everyday)
Hexadecimal | 16 | 0-9, A-F | 2AF₁₆ | Memory addresses, colors
Key: Subscript denotes the base. E.g., 1010₂ means 1010 in base 2 (binary).
C-CAT Tip: Hexadecimal uses A=10, B=11, C=12, D=13, E=14, F=15. Don't forget the letters!

## Slide 18
Powers of 2 — MEMORIZE THIS!
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
These values appear in almost EVERY C-CAT exam!
2⁰ | 2¹ | 2² | 2³ | 2⁴ | 2⁵ | 2⁶ | 2⁷ | 2⁸ | 2⁹ | 2¹⁰
1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024
Key Relationships:
1 Byte = 8 bits | 1 KB = 1024 Bytes | 1 MB = 1024 KB | 1 GB = 1024 MB | 1 TB = 1024 GB
1 Nibble = 4 bits | 1 Word = 16/32/64 bits (depends on architecture)
C-CAT Tip: 2¹⁰ = 1024 (not 1000!). This is why 1 KB = 1024 bytes. Also know: 2¹⁶ = 65536, 2²⁰ = 1048576.

## Slide 19
Conversion: Decimal to Binary (Division Method)
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
Convert 45₁₀ to Binary
Method: Divide by 2 repeatedly, note remainders
Division | Quotient | Remainder
45 ÷ 2 | 22 | 1
22 ÷ 2 | 11 | 0
11 ÷ 2 | 5 | 1
5 ÷ 2 | 2 | 1
2 ÷ 2 | 1 | 0
1 ÷ 2 | 0 | 1
Read remainders BOTTOM to TOP:
↑ 1 0 1 1 0 1
Answer: 45₁₀ = 101101₂
C-CAT Tip: Always read remainders from BOTTOM to TOP. The last remainder is the MSB (Most Significant Bit).

## Slide 20
Conversion: Binary to Decimal (Position Value Method)
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
Convert 101101₂ to Decimal
Position 5 | Position 4 | Position 3 | Position 2 | Position 1 | Position 0
1 | 0 | 1 | 1 | 0 | 1
2⁵=32 | 2⁴=16 | 2³=8 | 2²=4 | 2¹=2 | 2⁰=1
1×32=32 | 0×16=0 | 1×8=8 | 1×4=4 | 0×2=0 | 1×1=1
Sum: 32 + 0 + 8 + 4 + 0 + 1 = 45₁₀
C-CAT Tip: Multiply each bit by its positional power of 2, then add all products. Rightmost position = 2⁰.

## Slide 21
Binary ↔ Octal: Group in 3s
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
= | = | = | = | = | = | = | =
000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
Example: Convert 110101011₂ to Octal
Step 1: Group binary digits in sets of 3 (from right): 110 | 101 | 011
Step 2: Convert each group: 110 = 6 | 101 = 5 | 011 = 3
Answer: 110101011₂ = 653₈
C-CAT Tip: Octal uses 3-bit groups. Always group from RIGHT to LEFT. Pad with leading zeros if needed.

## Slide 22
Binary ↔ Hexadecimal: Group in 4s
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F
= | = | = | = | = | = | = | = | = | = | = | = | = | = | = | =
0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000 | 1001 | 1010 | 1011 | 1100 | 1101 | 1110 | 1111
Remember: A=10, B=11, C=12, D=13, E=14, F=15 (Purple columns above)
Example: Convert 10101111₂ to Hexadecimal
Group in 4s from right: 1010 | 1111 → A | F → AF₁₆
C-CAT Tip: Hex uses 4-bit groups. Each hex digit = exactly 4 binary bits. Group from RIGHT to LEFT!

## Slide 23
Binary Addition — Rules & Worked Example
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
Binary Addition Rules
0 + 0
=
0
0 + 1
=
1
1 + 0
=
1
1 + 1
=
10 (write 0, carry 1)
1 + 1 + 1
=
11 (write 1, carry 1)
Worked Example: 1011 + 1101
Carries: 1 1 1 1 0
1 0 1 1
+ 1 1 0 1
────────
1 1 0 0 0
Verify: 1011(11) + 1101(13) = 11000(24) ✓
C-CAT Tip: 1+1=10 in binary (not 2!). Always work right to left. Don't forget to carry!

## Slide 24
2's Complement — Representing Negative Numbers
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
How is -5 stored in 8-bit binary?
Step 1: Write +5 in binary
0 0 0 0 0 1 0 1
Step 2: Flip ALL bits
1 1 1 1 1 0 1 0
Step 3: Add 1
1 1 1 1 1 0 1 1
2's Complement Formula: Flip all bits + Add 1 = Negative number representation
-5 in 8-bit 2's complement = 11111011
C-CAT Tip: 2's complement = Flip bits + Add 1. MSB (leftmost bit) = sign bit (0=positive, 1=negative).

## Slide 25
2's Complement — Range of Values
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
Range Formula: – 2ⁿ⁻¹ to + 2ⁿ⁻¹ – 1 (where n = number of bits)
Bits (n) | Min Value | Max Value | Total Values
4 bits | -8 | +7 | 16
8 bits | -128 | +127 | 256
16 bits | -32,768 | +32,767 | 65,536
32 bits | -2,147,483,648 | +2,147,483,647 | 4,294,967,296
C-CAT TRAP: For 8-bit: 255 is the max for UNSIGNED representation (0 to 255). For 2's complement (SIGNED), it's -128 to +127. Don't mix them up!

## Slide 26
BCD vs. Binary — Know the Difference!
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
Represent the decimal number 59 in both BCD and Binary
BCD (Binary Coded Decimal)
Each decimal digit encoded separately:
5 → 0101 | 9 → 1001
BCD of 59 = 0101 1001
(8 bits total — 4 bits per digit)
VS
Pure Binary
Entire number converted at once:
59 ÷ 2 repeatedly...
Binary of 59 = 111011
(6 bits total — whole number converted)
THESE ARE DIFFERENT! BCD(59) = 01011001 vs Binary(59) = 00111011. C-CAT frequently tests this distinction!

## Slide 27
Day 1 — Quick Revision Summary
Day 1: Computer Evolution, Architecture & Number Systems | C-CAT Prep
Computer Generations
• 1st: Vacuum Tubes (ENIAC)
• 2nd: Transistors (IBM 1401)
• 3rd: ICs (IBM 360)
• 4th: Microprocessors / VLSI
• 5th: AI / ULSI
CPU Architecture
• CPU = ALU + CU + Registers
• ALU: Arithmetic & Logic ops
• CU: Fetches, decodes, controls
• Key Registers: PC, IR, ACC, MAR, MDR
System Bus
• Address Bus: Unidirectional (CPU→Mem)
• Data Bus: Bidirectional
• Control Bus: Bidirectional
Memory
• Hierarchy: Registers > Cache > RAM > HDD
• Volatile: RAM, Cache (lost on power off)
• Non-Volatile: ROM, HDD, SSD (retained)
Number Systems
• Binary(2), Octal(8), Decimal(10), Hex(16)
• 2's Complement = Flip bits + Add 1
• 8-bit signed range: -128 to +127
• BCD ≠ Binary (different encoding!)
C-CAT Tip: Review these key facts before the exam. Focus on generation technologies, bus directions, and number system conversions!